## Slide 1: Competitive Cyber Security Organization
Physical Security Workshop
By attending today’s meeting you acknowledge that you may be photographed or recorded for club use

## Slide 2: Learning Objectives:
Nondestructive Entry
  Lockpicking brief + demo
  Hands on time during other talks
Vehicle Security
Alarms + Handcuffs
Social Engineering
SERE

## Slide 3: Safety Disclaimer
We're teaching skills for the purpose of education and protection
Know the law; depending on your state some of these tools carry a felony for simple possession or intent
Some techniques may cause damage, do not practice on equipment that you don't own
We do not endorse any criminal activity

## Slide 4: Nondestructive Entry w Liam :)
Lockpicking, Bypassing Locks and Doors

## Slide 5: Learning Objectives
Types of locks
Lockpicking
  Single pin
  Rakes + Tools
Bypassing locks
  Shims
  Traveler's hooks
  Door mechanisms

## Slide 6: Common Lock Types
Pin and Tumbler
  Most doors in the US
Wafer
  Cars, Lockers
Tubular
  Bikes, Vending Machines
Disc Detainer
Warded
Lever

## Slide 7: More Lock Pictures

## Slide 8: Pin Tumbler Locks
Cylinder, Keyway, Driver Pin, Key Pin, Springs
Keys move pins to the shear line + turn the lock
Security pins + anti picking measurements

## Slide 9: Picking Pin Tumbler Locks
Preys on manufacturing tolerances
Apply turning force
Go through pins until they bind
Rinse and repeat

## Slide 10: Rakes, Jigglers, and Bumping
Not precise, quickly move pins into position

## Slide 11: Bypassing Locks
Unshielded keyways
Combing
Padlock Shimming
Decoding + Impressioning

## Slide 12: Bypassing Doors
Doors that open away from you
  Shims
Doors that open towards you
  Jims
  Traveler hooks
Under the door tools
Air Wedges

## Slide 13: Vehicle Security w Evan :D
Bypassing Vehicle Security

## Slide 14: Learning Objectives
Types of Vehicles and Locks
  Physical Key
  Keyless Entry
Starting the Vehicle
  Physical Key
  Key Fob
  Mobile Start
Prevention

## Slide 15: Vehicles With No Security
Skid Steers, Tractors, Lawnmowers
  Universal Key
ATV's and UTV's
  Pick the lock which only turns the battery on
  Screwdriver

## Slide 16: Manual Car Door Lock
Wafer Lock
Programmed Key Fob
Sensitive to Lock picks
  Strip Easily

## Slide 17: Keyless Entry
Unlock and Lock Signal
  Copy and re-transmit it
  Rolling and Non-Rolling
Signal Booster
  Tricks the car that the key fob is near the car
  Allows for unlocking and starting the engine

## Slide 18: Mobile Start
Start, Stop, and Unlock the Vehicle
Track Location
Full control of the Car
Smartphone Key Fob technology

## Slide 19: On-Star Attack
General Motors mobile assistant
5 years to fix full takeover 5 million cars
GM uses Verizon Servers
  Connect to the system through Verizon's voice network
  Copy an Mp3 file and reverse engineered it
  Create a file that overflows the computer and allows complete access through iOS

## Slide 20: Prevention
Don’t leave keys near windows
Leave Car Locked
Secure your doors
Park in the garage

## Slide 21: Handcuffs and houses
W/ Alec

## Slide 22: Learning Objectives
How to break out of handcuffs
Alarm Systems

## Slide 23: Handcuffs ;)
Proper Application?
Double lock

## Slide 24: Defeat handcuffs
Bobby Pin

## Slide 25: Defeat handcuffs
Shims

## Slide 26: Alarms
Defcon 29:
  Bill Graydon - Defeating Physical Intrusion Detection Alarm Wires
At home & at work

## Slide 27: Bypass da alarm
https://www.bypassvillage.org/games/alarm_wire/

## Slide 28: Use of alarms
Make noise, scare bad person
Indicator of issue
Alarm != Evidence; get a camera

## Slide 29: Social Engineering w Jenna >:)
Physical Phishing and exploiting humans

## Slide 30: Learning Objectives
What is Social Engineering?
Impersonating someone
Building a narrative
I'm in
Prevention

## Slide 31: What is Social Engineering?
Exploiting humans to gain entry or information
  Humans can be easily manipulated by taking advantage of their natural inclination
  Use social norms to your advantage
  If your emotions are running high, you are more likely to make a rash decision

## Slide 32: Impersonating Someone
Acting like you belong when you really don't
  Essentially creating a character and acting out the role
  Fake IT guy, janitor, etc.
Tailgating
  This happens all the time even here at PSU, especially in the dorms
  Even more susceptible if your hands are full
    Coffee cups
The key is to act with confidence

## Slide 33: Building a Narrative
More information = better narrative
Dumpster diving
  Sensitive information might not have been disposed of properly
  Can find device serial numbers, passwords, etc.
Shoulder surfing
  Can be from up close or from a distance
These can help build a narrative

## Slide 34: I'm in
After obtaining entry into a building, what next?
  Steal information
    Employee workstations left unlocked
    Creds on post-its
    Sensitive documents on desks
  Cause chaos
    Rubber duckies
    Physical access to hardware

## Slide 35: Prevention
Security is all about knowing who to trust
  Double check ID/identities
  Don't be afraid to question suspicious actors
Make sure information is disposed of properly
Keep desks and workspaces clear
Make others aware
Trust your gut

## Slide 36: SERE w Korbin ;)
Survival, Evasion, Resistance, and Escape

## Slide 37: What is SERE?
Is a course for people that are at extreme risk of capture and exploitation.
  Aircrew, Special Operations, Intelligence, and Diplomatic Personnel
SERE was formally recognized as a course after the Vietnam War.

## Slide 38: What is taught?
Survival
  How to survive in any biome.
Evasion
  How to evade capture in given setting.
Resistance
  How to resist interrogation tactics.
Escape
  How to either talk or break out of where you are being held.